## Slide 1
Sl No. | Part No. | Part Name
1 | FT100100 (NGC FH) | GLASS WINDSHIELD
2 | F1104300 (G90 FH) | GLASS WIND SHIELD
3 | X5R01400 (ACT FH) | GLASS WINDSHIELD
QR Code Sticker Details: | Remarks
1. Overall size of sticker | 50*25 mm
2. Sticker material | High gloss opaque polyester
3. QR code size | 10*10 mm
4. Gap all around | 3 mm
Sl. No. | Provisions in QR Code | Mandatory Field
1 | Supplier Code | 7200976
2 | Part Number | Refer part matrix
3 | Serial Number | Yes
4 | Date of Mfg | Yes
5 | Batch Code | Production Shift (A, B & C)
6 | Heat Code | NA
7 | Material Code | NA
8 | Drawing level | #
9 | Part Description | Glass_Windshield (15 Digits)
10 | Tier 1 Supplier | AIS
Part Matrix
QR Code Details
QR Code Specification : Ashok Leyland, Pantnagar

## Slide 2
QR Code Specification : Ashok Leyland, Pantnagar
25 mm
Supplier code $ Part No. $ Serial No. $ Date of Mfg. $ Batch code $ Heat code $ Material code $ Drawing level
$ Part description $ Supplier Name$
7200976$FT100100$0123$08.09.2021$A$NA$NA$#$WINDSHIELD$AIS$
Total Digit: 58 Nos.
50 mm
10 mm
10 mm
Part No.- FT100100
Part Name- Windshield
Serial No. – XXXX
Date of Mfg. – XX.XX.XXXX
Supplier - Asahi India Glass Limited
Information in Vacant area:
Sample QR Code Sticker
Gap 03 mm all around

## Slide 3: QR Code Sticker Requirements: AL
Sl No. | Part No. | Part Name
1 | FT100100 (NGC FH) | GLASS WINDSHIELD
2 | F1104300 (G90 FH) | GLASS WIND SHIELD
3 | X5R01400 (ACT FH) | GLASS WINDSHIELD
7200976$FT100100$0001$27.10.2021$A$NA$NA$#$WINDSHIELD$AIS$
Part No.- FT100100
Part Name- Windshield
Serial No. – 0001
Date of Mfg. – 27.10.2021
Asahi India Glass Limited
QR Code Input: Model 1
Information in Vacant area:
Model: 1
7200976$F1104300$0001$05.10.2021$A$NA$NA$#$WINDSHIELD$AIS$
Part No.- F1104300
Part Name- Windshield
Serial No. – 0001
Date of Mfg. – 05.10.2021
Asahi India Glass Limited
QR Code Input: Model 2
Information in Vacant area:
Model: 2
7200976$X5R01400$0001$18.10.2021$A$NA$NA$#$WINDSHIELD$AIS$
Part No.- X5R01400
Part Name- Windshield
Serial No. – 0001
Date of Mfg. – 18.10.2021
Asahi India Glass Limited
QR Code Input: Model 3
Information in Vacant area:
Model: 3
QR Sticker Quantity: 300 Nos.
QR Sticker Quantity: 300 Nos.
QR Sticker Quantity: 500 Nos.