## Slide 1
Asahi India Glass Limited
QR Code Implementation – TML Jamshedpur

## Slide 2
QR Code Specification & Proposal
Sl. No. | Parameter | QR Code Sticker Detail | Remarks
1 | QR code label size | 15.5 ± 1.0 X 15.5 ± 1.0 mm | 
2 | QR code sticker size | 20.0 ± 1.0 X 25.0 ± 1.0 mm | 
3 | QR code background and letters | Letters are in black color, background in white color | 
4 | Sticker material | High gloss opaque polyester | 
5 | Information with QR code |  | 
6 | QR code location on Glass | QR CODE STICKER TO BE GLUED ON WINDSHIELD INNER SURFACE QR CODE WILL BE READABLE FROM INSIDE | 
7 | QR Code position tolerance | Shifting ± 8.0 mm Alignment ± 5.0 mm | 

## Slide 3
QR Code Specification given in Drawing
(Model Signa & Prima Windshield, TML Jamshedpur)
Sl No. | Model | Part No. | AIS Code | Part Name | Drawing Revision No.
1 | Prima | 281667102302 | TWC FH | GLASS WINDSCREEN | C
2 | Prima | 281672502301 | TWC FDL | Door Glass | D
3 | Prima | 281672502302 | TWC FDR | Door Glass | D
4 | Signa | 257667102316 | TTS FH | GLASS WINDSCREEN | P
5 |  | 268067102304 | TTB FH | GLASS WINDSCREEN | I
6 |  | 257672502303 | TTS SRL | GLASS PANE REGULATING WINDOW | M
7 |  | 268072502303 | TTS-RQR | GLASS PANE QUARTER WINDOW RH | G
8 |  | 268072502302 | TTS-RQL | GLASS PANE QUARTER WINDOW LH | G

## Slide 4
QR Code Sticker Design Proposal – TML Jamshedpur
QR Code Printing Detail- Prima (For reference) |  |  |  |  | 
Sr No. | Description |  |  |  | 
 | TML Part Number | Revision Level | TML Vendor Code | Mfg Date | Component Serial Number
1 | 00281667102302 | C0 | A65681 | 0921 | 000001
2 | 00281667102302 | C0 | A65681 | 0921 | 000002
3 | 00281667102302 | C0 | A65681 | 0921 | 000003
4 | 00281667102302 | C0 | A65681 | 0921 | 000004
5 | 00281667102302 | C0 | A65681 | 0921 | 000005
6 | 00281667102302 | C0 | A65681 | 0921 | 000006
7 | 00281667102302 | C0 | A65681 | 0921 | 000007
8 | 00281667102302 | C0 | A65681 | 0921 | 000008
9 | 00281667102302 | C0 | A65681 | 0921 | 000009
10 | 00281667102302 | C0 | A65681 | 0921 | 000010
11 | 00281667102302 | C0 | A65681 | 0921 | 000011
12 | 00281667102302 | C0 | A65681 | 0921 | 000012
13 | 00281667102302 | C0 | A65681 | 0921 | 000013
14 | 00281667102302 | C0 | A65681 | 0921 | 000014
15 | 00281667102302 | C0 | A65681 | 0921 | 000015
20± 1 mm
15.5 ± 1 mm
15.5 ± 1 mm
25 ± 1 mm
Information in Vacant area:
00281667102302C0A656811121000001
After QR Scanning:
281667102302
000001
TWC FH 1121
Asahi India Glass Limited

## Slide 5: Sample Sticker Details
5
QR Code Sticker sample requirements |  |  |  |  |  | 
Sl No. |  | QR Input |  |  |  | 
 | Model | TML Part Number | Revision Level | TML Vendor Code | Mfg Date | Component Serial Number
1 | Prima (TWC FH) | 00281667102302 | C0 | A65681 | 1021 | 000001
2 | Signa (TTS FH) | 00257667102316 | P0 | A65681 | 1021 | 000001
3 | Signa (TTB FH) | 00268067102304 | I0 | A65681 | 1021 | 000001
00281667102302C0A656811121000001
QR Code Input: Model 1
00257667102316P0A656811121000001
QR Code Input: Model 2
00268067102304I0A656811121000001
QR Code Input: Model 3
281667102302
000001
TWC FH 1121
Asahi India Glass Limited
268067102304
000001
TTB FH 1121
Asahi India Glass Limited
257667102316
000001
TTS FH 1121
Asahi India Glass Limited
Information in Vacant area:
Model: 1
Model: 3
Model: 2

## Slide 6: Sample Glass Dispatch Details
6
QR Code Sticker sample glass |  |  |  |  |  | 
Sl No. | Model | AIS Code | TML Part Number | Sample Qty. | Pallet No. | QR Code Sticker Picture
1 | Signa | TTS FH | 257667102316 | 05 Nos. | XXN 182 | 
2 | Signa | TTB FH | 268067102304 | 05 Nos. | XXN 115 | 
3 | Prima | TWC FH | 281667102302 | 05 Nos. | XXL 038 | 

## Slide 7
QR Code Sticker Design Proposal – TML Jamshedpur
20± 1 mm
15.5 ± 1 mm
15.5 ± 1 mm
25 ± 1 mm
Information in Vacant area:
00281672502301D0A656810722000001
After QR Scanning:
281672502301
000001
TWC-FDL
0722
Asahi India Glass Limited
QR Code Sticker sample requirements |  |  |  |  |  | 
Sl No. |  | QR Input |  |  |  | 
 | Model | TML Part Number | Revision Level | TML Vendor Code | Mfg Date | Component Serial Number
1 | World Truck/Prima (TWC-FDL) | 00281672502301 | D0 | A65681 | 0722 | 000001
2 | World Truck/Prima (TWC-FDR) | 00281672502302 | D0 | A65681 | 0722 | 000001
281672502302
000001
TWC-FDR
0722
Asahi India Glass Limited
00281672502302D0A656810722000001
After QR Scanning:

## Slide 8
QR Code Sticker Design Proposal – TML Jamshedpur
20± 1 mm
15.5 ± 1 mm
15.5 ± 1 mm
25 ± 1 mm
Information in Vacant area:
00257672502303M0A656810722000001
After QR Scanning:
257672502303
000001
TTS SRL 0722
Asahi India Glass Limited
QR Code Sticker sample requirements |  |  |  |  |  | 
Sl No. |  | QR Input |  |  |  | 
 | Model | TML Part Number | Revision Level | TML Vendor Code | Mfg Date | Component Serial Number
1 | Signa (TTS-SRL) | 00257672502303 | M0 | A65681 | 0722 | 000001

## Slide 9
QR Code Sticker Design Proposal – TML Jamshedpur
20± 1 mm
15.5 ± 1 mm
15.5 ± 1 mm
25 ± 1 mm
Information in Vacant area:
00268072502303G0A656810722000001
After QR Scanning:
268072502303
000001
TTS- RQR 0722
Asahi India Glass Limited
QR Code Sticker sample requirements |  |  |  |  |  | 
Sl No. |  | QR Input |  |  |  | 
 | Model | TML Part Number | Revision Level | TML Vendor Code | Mfg Date | Component Serial Number
1 | Signa (TTS-RQR) | 00268072502303 | G0 | A65681 | 0722 | 000001
2 | Signa (TTS-RQL) | 00268072502302 | G0 | A65681 | 0722 | 000001
268072502302
000001
TTS- RQL 0722
Asahi India Glass Limited
00268072502302G0A656810722000001